## Slide 1: Hydrodynamics
Physics 1425 Lecture 27
Michael Fowler, UVa

## Slide 2: Basic Concepts
Fluid conservation
Bernoulli’s Equation

## Slide 3: You are sitting in a rowing boat in a small pond. There are some bricks in the boat. You take the bricks and throw them into the pond. They sink to the bottom. What happens to the water level in the pond, as measured at the bank?
It falls.
It rises.
It stays the same.

## Slide 4: Fluid Flow: Laminar and Turbulent
In laminar or streamline flow, each particle of fluid follows a smooth path, the streamline.
Air flow over this Corvette is laminar until the end: the air cannot curve in completely at the back, it breaks away forming a turbulent wake.

## Slide 5: Conservation of Fluid
Suppose fluid is flowing steadily through a pipe which has a narrow section.
The rate of flow, gallons per sec or cubic meters per sec, must be the same past a point in the narrow part as past a point in the wide part—or fluid will be piling up somewhere!
So it flows faster through the narrow part.
area A1 area A2
Imagine a short cylinder of the fluid, of length Δℓ1 in the wide part—as it squeezes into the narrow part it gets longer.
The total mass of fluid Δm in the short cylinder is density x area x length, so
Δm = ρΔV = ρ1A1Δℓ1 = ρ2A2Δℓ2
Δℓ1
Δℓ2

## Slide 6: Fluid Velocity: Equation of Continuity
If the fluid flows distance Δℓ1 in the wide tube in time Δt, the mass flow rate past a point is Δm/Δt = ρ1A1Δℓ1/ Δt = ρ1A1v1.
Since the mass flow rate through area A1 must equal that through A2 for steady flow,
ρ1A1v1 = ρ2A2v2
the “equation of continuity” and often the ρ’s can be dropped—water is essentially incompressible, and at low speeds so is air.
Δℓ1
Δℓ2
Area A1
Area A2

## Slide 7: Clicker Question
Where will the pressure be greatest in steady fluid flow?
The entering wide part
The central narrow part
The final wide part
A
B
C

## Slide 8: Clicker Answer
Where will the pressure be greatest in steady fluid flow?
The portion of fluid speeds up as it enters the narrow part—this can only happen if it’s pushed from behind. This means the pressure behind is greater.
As it leaves the narrow part, it slows down: again, the pressure is greater in the wide part.
A
B
C

## Slide 9: Bernoulli’s Equation
Focus now on the block of fluid that’s between A1 and A2 at one instant in time.
After time Δt, that same fluid will now be between the downstream areas A´1 and A´2, and it’s picked up some KE!
A mass Δm = ρ1A1Δℓ1 moving at v1 has been replaced by mass ρ2A2Δℓ2 moving faster—at v2. From continuity, these masses are the same—so taking ρ constant, there is a KE gain of
½Δm(v22 – v12) = ½ρA1Δℓ1(v22 – v12).
Δℓ1
Δℓ2
Area A1
Area A2
Area A´2
Area A´1

## Slide 10: Bernoulli’s Equation
In the time Δt, there is a KE gain of ½ρA1Δℓ1(v22 – v12).
Where did that energy come from?
In the time Δt, the pressure P1 on the area A1 does work:
force x distance = P1A1Δℓ1
BUT at the same time, our block of fluid did some work itself: it pushed the fluid in front of it, doing work = P2A2Δℓ2.
SO net work done = (P1 - P2) A1Δℓ1 =KE gain ½ρA1Δℓ1(v22 – v12)
That is, P1 + ½ρv12 = P2 + ½ρv22
Δℓ1
Δℓ2
Area A1
Area A2
Area A´2
Area A´1
Pressure P1
For constant density, A1Δℓ1 =A2Δℓ2

## Slide 11: Uphill Work…
What if the pipe is tilted upwards?
Now the pressure speeding the fluid along has to lift it as well!
So the pressure adds potential energy corresponding to how much it was lifted as well as kinetic energy from speeding it up.
This gives the full Bernoulli’s equation:
P1 + ½ρv12 + ρgy1= P2 + ½ρv22 + ρgy2
V
x
y
(vertical)

## Slide 12: I hold two sheets of paper hanging from my hands parallel, one or two inches apart. I blow between the two sheets. What happens?
They move towards each other.
They move apart.

## Slide 13: Torricelli’s Theorem
Water coming from a small spigot in a large tank has a speed given by
v2 = 2gh
This is a special case of Bernoulli’s equation, because the outside pressure at the spigot is the same as that at the top of the fluid, and fluid velocity at the top is negligible.
x
h