## Slide 1: Capacitors II
Physics 2415 Lecture 9
Michael Fowler, UVa

## Slide 2: Today’s Topics
First, some review… then
Storing energy in a capacitor
How energy is stored in the electric field
Dielectrics: why they strengthen capacitors

## Slide 3: Parallel Plate Capacitor
E = /0 = Q/A0 and V = Ed,
so
a
area A
d apart
d apart
Q
_
_
_
_
_
_
-Q
+
+
+
+
+
+
+
Charge will settle on inside surfaces
_
Know this formula!

## Slide 4: Capacitors in Parallel
Let’s look first at hooking up two identical parallel plate capacitors in parallel: that means the wires from the two top plates are joined, similarly at the bottom, so effectively they become one capacitor.
What is its capacitance? From the picture, the combined capacitor has twice the area of plates, the same distance apart.
We see that C = C1 + C2
a

## Slide 5: Capacitors in Parallel
If two capacitors C1, C2 are wired together as shown they have the same voltage V between plates.
Hence they hold charges Q1 = C1V, Q2 = C2V, for total charge Q = Q1 + Q2 = (C1 + C2)V = CV.
So capacitors in parallel just add:
C = C1 + C2 + C3 + …
C1
C2

## Slide 6: Capacitors in Series
Regarding the above as a single capacitor, the important thing to realize is that in adding charge via the outside end wires, no charge is added to the central section labeled A: it’s isolated by the gaps between the plates.
Charge Q on the outside plate of C1 will attract –Q to the other plate, this has to come from C2, as shown.
Series capacitors all hold the same charge.
Q
Q
-Q
-Q
A
C2
C1

## Slide 7: Capacitors in Series
Series capacitors all hold the same charge.
The voltage drop V1 across C1 is V1 = Q/C1.
The voltage drop across C2 is V2 =Q/C2.
Denoting the total capacitance of the two taken together as C, then the total voltage drop is V = Q/C.
But V = V1 + V2, so Q/C = Q/C1 + Q/C2,
Q
Q
-Q
-Q
A
C2
C1
Important!

## Slide 8: It Takes Work to Charge a Capacitor
Suppose a sphere capacitor C already contains charge q. Then it’s at a potential V(q) = q/C.
To bring a further little charge dq from far away, against the repulsive force of the charge already there, takes work V(q)dq.
So, to deliver a total charge Q to the capacitor, one bit dq at a time, takes total work:

## Slide 9: Work Done in Charging a Parallel Plate Capacitor
The math is identical to charging a sphere by bringing up little charges from far away (see the last slide) but for the parallel plate capacitor we only have to bring charge across from one plate to another: the work is still V(q)dq for each dq.
A capacitor is actually charged, of course, by using a battery to pump charge from one plate to the other via an outside wire, but the route taken doesn’t affect the gain in potential energy of the charge transferred.
q
+
+
+
+
+
+
+
+
+
+
+
+
_
_
_
_
_
_
_
_
_
_
_
_
dq
q
-q
V(q) = q/C

## Slide 10: Energy Stored in a Capacitor
The work needed to place charge in a capacitor is stored as electrostatic potential energy in the capacitor:
We proved the first, the others come from V = Q/C.

## Slide 11: Clicker Question
How much work does it take to put charge Q on to a 2mF capacitor compared with putting the same charge on to a 1mF capacitor?
Twice as much
The same
Half as much

## Slide 12: Clicker Answer
How much work does it take to put charge Q on to a 2mF capacitor compared with putting the same charge on to a 1mF capacitor?
Half as much: the 2mF capacitor is only at half the voltage of the 1mF capacitor if they have the same charge q, so bringing up extra charge dq takes only half the work.

## Slide 13: Pulling the Plates Apart
Suppose we have charge Q on a parallel plate capacitor having area A and plate separation d.
We now pull the plates to a greater distance apart, say 2d.
Assume first that the capacitor is disconnected from the battery, so no charge can flow.
Since the plates are oppositely charged, it takes work to pull them apart.
a

## Slide 14: Field for Two Oppositely Charged Planes
a
+
=
Superpose the field lines from the negatively charged plate on the parallel positively charged one, and you’ll see the total field is double in the space between the plates, but exactly zero outside the plates.
Reminder from lecture 3

## Slide 15: Working to Pull the Plates Apart
From the last slide, the electric field E = /0 between the plates is /20 from the top plate and /20 from the bottom plate.
Therefore, in finding the work done against the electric field in moving the top plate, charge Q, we can only count the field from the bottom plate—a charge can’t do work moving in its own field!
a

## Slide 16: Working to Pull the Plates Apart
Moving the top plate, charge Q = A, a distance x outwards in the electric field /20 from the bottom plate takes work
Now initially , finally
so work done = capacitor energy change:
a
a
x

## Slide 17: Working to Pull the Plates Apart
Moving the top plate, charge Q, a distance x outwards created an extra volume V = Ax between the plates, filled with the constant electric field E, and took work:
The electric field itself is the store of energy: and this is true in general, for varying as well as constant fields, the energy density in an electric field is
a
x

## Slide 18: Clicker Question
Suppose the parallel plates are pulled apart from separation d to 2d, the plates having a constant potential difference V from a battery.
What happens to the electric field strength between the plates?
It’s doubled
It’s halved
It’s constant
a
V
V

## Slide 19: Clicker Answer
Suppose the parallel plates are pulled apart from separation d to 2d, the plates having a constant potential difference V from a battery.
What happens to the electric field strength between the plates?
It’s doubled
It’s halved
same voltage, double distance: V/m.
a
V
V

## Slide 20: Clicker Question
Suppose the parallel plates are pulled apart from separation d to 2d, the plates having a constant potential difference V from a battery.
What happens to the total energy stored in the capacitor?
It’s doubled
It’s halved
It’s constant
It increases by a factor of 4
It decreases by a factor of 4
a
V
V

## Slide 21: Clicker Answer
Suppose the parallel plates are pulled apart from separation d to 2d, the plates having a constant potential difference V from a battery.
What happens to the total energy stored in the capacitor?
It’s doubled
It’s halved
It’s constant
It increases by a factor of 4
It decreases by a factor of 4
a
V
V

## Slide 22: Puzzle…
Pulling the plates apart takes external work, since the plates are oppositely charged and attract each other.
Yet after pulling them to double the initial separation, there is less energy stored in the capacitor than before!
What about conservation of energy?
a
V
V

## Slide 23: Puzzle Answer
What about conservation of energy?
The capacitance goes down, the voltage is constant, so charge flows from the capacitance into the battery. (Q = CV)
And, it flows the wrong way—against the battery’s potential, so this takes work. The battery is being charged, it’s storing energy.
a
V
V

## Slide 24: Field Energy for a Charged Sphere
For a charged spherical conductor of radius R:
The energy stored in the electric field is
and this is just , so the capacitor’s energy is in the electric field.

## Slide 25: How Big is an Electron?
We’ve just seen that a charge Q on a sphere of radius R has electric field energy
This means that since the electron has a charge, if the inverse square law holds up at smaller and smaller distances, it can’t be infinitely small!
A lower limit on its size is given by assuming its mass comes entirely from this electrostatic energy, using U = E = mc2.
This gives R about 10-15m: called the classical radius of the electron. In fact, at this R, Coulomb’s law breaks down—and we need quantum mechanics.

## Slide 26: Dielectrics
If a nonconducting material is placed in an electric field, the electrons will still move a little, remaining within their home molecules or atoms, which will therefore become polar.
The overall effect of this polarization is to generate a layer of positive charge on the right and negative charge on the left.
a
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_

## Slide 27: Dielectrics
If a nonconducting material is placed in an electric field, the electrons will still move a little, remaining within their home molecules or atoms, which will therefore become polar.
The overall effect of this polarization is to generate a layer of positive charge on the right and negative charge on the left.
a
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
+
+
+
+
+
_
_
_
_
_
_

## Slide 28: Dielectrics
These “layers of surface excess charge” created by the polarization generate an electric field opposing the external field.
However, unlike a conductor, this field cannot be strong enough to give zero field inside, because then the polarization would all go away.
a
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
_
+
+
+
+
+
+
_
_
_
_
_
_